## Slide 1: Computational Proteomics and Metabolomics
Oliver Kohlbacher, Sven Nahnsen, Knut Reinert
4. Quantification I: General concepts, isobaric tags

## Slide 2: Overview
Quantification using mass spectrometry
  Basic terms from analytical chemistry
  Quantitative behavior of mass spectrometers
Experimental quantification strategies
    Absolute and relative quantification
    Label-free vs. labeled techniques
    Selected experimental techniques
    Isobaric tags

## Slide 3: Analytical Chemistry
“Analytical chemistry is the study of the separation, identification, and quantification of the chemical components of natural and artificial materials.”
“Quantification […] is the act of counting and measuring that maps human sense observations and experiences into members of some set of numbers.”
Quantitative Mass Spectrometry :=
  use of a mass spectrometer to turn amounts of analytes into numbers
http://en.wikipedia.org/wiki/Analytical_chemistry [accessed 12.11.2011, 10:40 CET]
http://en.wikipedia.org/wiki/Quantification [accessed 12.11.2011, 10:45 CET]

## Slide 4: Some Terms
Analyte – the stuff we want to analyze (proteins, peptides, metabolites)
Matrix – the components of the sample that are not analytes
The matrix can significantly impact the way the whole analysis is performed
Example
  Proteomics analysis from urine
  Urine contains
    Proteins and peptides – the analytes
    Water
    Metabolites
    Urea
    …
matrix

## Slide 5: Matrix Effects in LC-MS
Components of the matrix are being separated just like the analytes
Parts of the matrix can be ionized as well and then also show up as signals in the MS
A priori it is unknown, which part of the signal stems from matrix or analytes
Matrix can interfere with the analysis by
  Competing with analytes for ionization -> reduce the number of analyte molecules ionized
  Adsorb, precipitate or even react with the analyte

## Slide 6: Quantifying Analytes
Analytes have to be in solution for proteomics and metabolomics
We thus deal with concentrations: amounts per volume of sample V
Molar concentration
  ci = ni / V [SI unit: mol/m3]
Mass concentration
  ρi = mi / V [SI unit: kg/m3]
Translating molar concentrations into mass concentrations can be done via the molecular weight Mi of the analyte
  ρi = ci Mi

## Slide 7: Precision and Accuracy
Accuracy: closeness to the true value (mostly influenced by systematic error) – repetition of the experiment will not improve the result
Precision: repeatability of the measurement (mostly influenced by random error) – repetition of the experiment will yield a value closer to the true value
An ideal experiment combines high accuracy with high precision
good accuracy,
poor precision
good precision,
poor accuracy

## Slide 8: Measurement Errors
Each measurement is associated with an error
There are two basic types of error:
  Random error: defines the variance of repeated measurements (e.g., due to high noise level) – this is always present in every measurement
  Systematic error (bias): shifts the mean of repeated experiments (e.g., due to an incorrect calibration)

## Slide 9: Calibration Curve
Measurement of the detector response for various (known) concentrations allows the construction of a calibration curve
Most detector responses are chosen in a way that the response changes linearly with the concentration
Once the calibration curve has been measured, it allows the determination of the concentration of an unknown sample
detector
response
concentration

## Slide 10: Response
LOD: level of detection – at what concentration can we decide that the analyte is present
LOQ: level of quantification – at what concentration can we accurately quantify it
LOL: limit of linearity – saturation effects start here
Linear range (dynamic range): the concentration range where we get a response that is linear in the concentration
detector
response
concentration
saturation
LOD
LOQ
LOL
linear range
slope = sensitivity
noise

## Slide 11: Detection Limit
Limit of detection (detection limit) -- LOD: the lowest analyte concentration that can be distinguished from the absence of the analyte (blank) within a stated confidence limit (generally 99% confidence)
Limit of quantification – LOQ: the concentration at which we can distinguish two values with reasonable confidence
Both depend on the noise level, the matrix, the instrument, the sensitivity for a specific analyte, etc.
http://en.wikipedia.org/wiki/Detection_limit [accessed 15.11.2011, 14:00 CET

## Slide 12: LOD/LOQ
“Suppose you are at an airport with lots of noise from jets taking off. If the person next to you speaks softly, you will probably not hear them. Their voice is less than the LOD. If they speak a bit louder, you may hear them but it is not possible to be certain of what they are saying and there is still a good chance you may not hear them. Their voice is >LOD but <LOQ. If they speak even louder, then you can understand them and take action on what they are saying and there is little chance you will not hear them. Their voice is then >LOD and >LOQ. Likewise, their voice may stay at the same loudness, but the noise from jets may be reduced allowing their voice to become >LOD. Detection limits are dependent on both the signal intensity (voice) and the noise (jet noise).”
http://en.wikipedia.org/wiki/Detection_limit [accessed 12.11.2011, 10:20 CET

## Slide 13: Quantitative Mass Spectrometry
Ionization: number of ionized analyte molecules proportional to the total amount present
MS detector: proportional to the number of ions (the ion current)
Caveats:
  Saturation: there is an upper limit to the response
  Noise: does the signal really come from the analyte?

## Slide 14: Quantitative LC-MS
Fixed volume of the sample is injected
Total amount of analyte eluting from the column is the same amount as the amount injected (normally, nothing gets ‘lost’ on the column)
Analyte spreads out, elutes over a certain timespan from the column: maximum concentrations at the end of the column depend on retention time (peak broadening)
Only a fraction of the analyte really enters the MS (skimmer!)
Ionization efficiency differs between analytes

## Slide 15: Quantitative LC-MS
MS signal intensity for peptide i at time t is proportional to concentration ci(t) eluting off the column.
The area under the (chromatographic) peak is proportional to the total amount citot of analyte eluting and thus to the amount in the sample. Hence we want to integrate over time.
Notes: LatexIT formula:
I_i(t) & = f_i\cdot \int_t c_i(t)
\int_t I_i(t) & = f_i\cdot \int_t c_i(t)

## Slide 16: Quantitative LC-MS
Elution profiles are (roughly) Gaussians. Hence we can model the the elution as a product of the total concentration spread by a retention time model
Strategy
  Integrate over the MS signal (intensity Ii(t)) caused by the analyte i over the total elution time of an analyte (centered around rti, peak width defined by standard deviation of the Gaussian)
  Response factor fi is unknown
Notes: LatexIT formula:
c_i(t) & = g(rt_i,\sigma_i,t)c^{tot}_i \\
\int_t I_i(t) & = f_i \cdot c^{tot}_i \cdot \int_t g(rt_i,\sigma_i,t) \\
\int_t I_i(t) & = f_i \cdot c^{tot}_i \cdot 1
0_i

## Slide 17: Detection, Identification, Quantification
Proteomics
  More peptides/proteins are usually identified than quantified
  Identification: MS/MS, quantification usually by MS -> independent processes
  Many things can be seen (detected) but cannot be identified or quantified
Metabolomics
  Identification here is particularly difficult
  We can identify only a fraction of what we can quantify
Bantscheff et al., Anal Bioanal Chem (2005), 389, 1017-1031.
LOQ
LOD
LOI
LOI: “Level of identification”

## Slide 18: Quantitative Data – MS Spectra
Different ionized species in the same MS spectrum result in different peaks
Example
  Each peptide leads to a distinct set of peaks (isotope patterns!)
  Intensity of each peak is proportional to the concentration at the time of elution

## Slide 19: Quantitative Data – MS Spectra
Direct comparison of intensities of different analytes in the same spectrum is not possible because they have different response factors!
Exception: peptides/metabolites that differ only by a stable isotope label will have identical response factors – their intensities can be compared within the same spectrum! This is the basis for isotopic labels.
light
heavy

## Slide 20: Quantitative Data – MS2 Spectra
Fragment spectra can be used for quantification as well
  Under identical fragmentation conditions, the fragment ion intensity is proportional to the parent ion concentration/intensity
  Key methods: MRM, iTRAQ
iTRAQ MS2 spectrum (4-plex) with reporter ions at 114, 115, 116, 117 Da (intensities roughly 0.6:0.6:1:1)

## Slide 21: Chromatograms
Except for quantification techniques where a direct comparison is made within the same spectrum (iTRAQ, SILAC), elution profiles have to be considered
Accurate quantification requires accurate integration over the retention time profile
Since the peak area remains the same, this means the quantification will be independent of changes in the peak shape and width
Elution profiles are often assumed to be Gaussian, but in reality they can deviate significantly (tailing/heading leads to asymmetric peak shapes – in the model of theoretical plates, this corresponds to incomplete equilibration)
For details, see Learning Unit 2A
Notes: Here ends the LU 4A

## Slide 22: Quantification Strategies
Quantitative Proteomics
Relative Quantification
Labeled
Label-Free
Absolute Quantification
AQUA
SISCAPA
Spectral Counting
Feature-Based
In vivo
In vitro
14N/15N
SILAC
iTRAQ
TMT
16O/18O
MRM
After: Lau et al., Proteomics, 2007, 7, 2787

## Slide 23: Labeling Techniques
Many labeling techniques exploit stable isotope labeling
  Different isotopes of the same element behave chemically basically identically (often used: 1/2H, 12/13C, 14/15N, 16/18O)
  Their masses differ, however, so the MS can distinguish them
Introducing a label in one sample and a different (or no label) in another, mixing allows a relative quantification between two (or more) samples
Advantages
  Both samples are treated identically, systematic errors affect them in the same way
  Can be easily annotated manually (e.g., look for pairs of peaks)
Disadvantages
  Labels can be expensive, difficult, unreliable to introduce
  Labeling in vivo is not always possible, not all techniques support in vitro labeling

## Slide 24: Labeling Techniques
Chemical labeling
  Peptides are modified chemically after extraction
  Label is usually attached covalently at specific functional groups (N-terminus, specific side chains, …)
  Does not involve a perturbation of the in vivo system
  Labeling occurs late (during sample preparation) and thus does not account for variance introduced in the early steps
Metabolic labeling
  Stable isotope labels are integrated by ‘feeding’ the organism with labeled metabolites (amino acids, nitrogen sources, glucose, …)
  Full incorporation of the label can take a while
  Requires perturbation of the in vivo system, depending on the size quite expensive
  Labeling occurs early in the study, results in higher reproducibility

## Slide 25: SILAC
SILAC – Stable Isotope Labeling with Amino Acids in Cell Culture
  Introduce stable labels by feeding labeled amino acids to the cell culture
  Labels will be integrated into all proteins after a reasonable amount of time
  Mix and compare with an unlabeled sample
  Tryptic digest ensures that each peptide contains at most one lysine!
  Peptides with heavy and light label are otherwise identical and coelute
  Spectra contain isotope patterns for both heavy and light peptides
SILAC pair with charge 2 and approximately a 1:1 ratio (unperturbed)
light
heavy

## Slide 26: SILAC
Ong, Mann, Nat Prot 1 (2007), 2650-2660.

## Slide 27: SILAC
Ong, Mann, Nat Prot 1 (2007), 2650-2660.

## Slide 28: SILAC
Ong, Mann, Nat Prot 1 (2007), 2650-2660.

## Slide 29: SILAC
Mumby, Brekken, Genome Biol (2005), 6:230

## Slide 30: Spike-In SILAC
Geiger et al., Nat Prot 6 (2011), 147-157.

## Slide 31: Spike-In SILAC
Geiger et al., Nat Prot 6 (2011), 147-157.

## Slide 32: SILAC Mouse
Krüger et al., Cell (2008), 134:353-364.

## Slide 33: Isobaric Labeling
http://en.wikipedia.org/wiki/File:Isobaric_labeling.png [accessed 19.11.11, 19:48 CET]

## Slide 34: Isobaric Labeling
Idea
  Label the different samples with labels of the same mass (isobaric)
  Design the label in a way that they fragment differently upon collision-induced dissociation
  MS2 spectra will then contain reporter ions
  Quantification and identification are then both based on tandem spectra only
Key method: iTRAQ – isobaric tags for relative and absolute quantification
  Based on covalent modification of N-terminus of peptides
  Labeling performed after digestion (also applicable to clinical samples)
  Kits available for 4 or 8 distinct labels (‘quadroplex’, ‘octoplex’)

## Slide 35: iTRAQ
Ross et al., Mol Cell Prot (2004), 3, 1154-1169.

## Slide 36: iTRAQ
Ross et al., Mol Cell Prot (2004), 3, 1154-1169.

## Slide 37: iTRAQ
Ross et al., Mol Cell Prot (2004), 3, 1154-1169.

## Slide 38: Quantitative Data – LC-MS Maps
Spectra are acquired with rates up to dozens per second
Stacking the spectra yields maps
Resolution:
  Up to millions of points per spectrum
  Tens of thousands of spectra per LC run
Huge 2D datasets of up to hundreds of GB per sample
MS intensity follows the chromatographic concentration

## Slide 39: LC-MS Data (Map)
  Quantification
  (15 nmol/µl, 3x over-expressed, …)

## Slide 40: Label-Free Quantification (LFQ)
Label-free quantification is probably the most natural way of quantifying
  No labeling required, removing further sources of error, no restriction on sample generation, cheap
  Data on different samples acquired in different measurements – higher reproducibility needed
  Manual analysis difficult
  Scales very well with the number of samples, basically no limit, no difference in the analysis between 2 or 100 samples

## Slide 41: LFQ – Analysis Strategy
Find features in all maps

## Slide 42: LFQ – Analysis Strategy
Find features in all maps
Align maps

## Slide 43: LFQ – Analysis Strategy
Find features in all maps
Align maps
Link corresponding features

## Slide 44: LFQ – Analysis Strategy
Find features in all maps
Align maps
Link corresponding features
Identify features
GDAFFGMSCK

## Slide 45: LFQ – Analysis Strategy
Find features in all maps
Align maps
Link corresponding features
Identify features
Quantify
GDAFFGMSCK
1.0 : 1.2 : 0.5

## Slide 46: Feature-Based Alignment
LC-MS maps can contain millions of peaks
Retention time of peptides and metabolites can shift between experiments
In label-free quantification, maps thus need to be aligned in order to identify corresponding features
Alignment can be done on the raw maps (where it is usually called ‘dewarping’) or on already identified features
The latter is simpler, as it does not require the alignment of millions of peaks, but just of tens of thousands of features
Disadvantage: it replies on an accurate feature finding

## Slide 47: Feature-Based Alignment
~350,000 peaks
~ 700 features

## Slide 48: Feature Finding
Identify all peaks belonging to one peptide
Key idea:
  Identify suspicious regions
  Fit a model to that region and identify peaks explained by it

## Slide 49: Feature Finding
Extension: collect all data points close to the seed
Refinement: remove peaks that are not consistent with the model
Fit an optimal model for the reduced set of peaks
Iterate this until no further improvement can be achieved

## Slide 50: Linear Alignment
Lange et al. proposed an efficient feature-based alignment of maps based on pose clustering
The algorithm takes a pair of maps and computes an optimal linear alignment
It can be applied for multiple alignment of an arbitrary amount of maps by applying it multiply and align the maps in a star-like fashion onto one reference map (k-1 alignments for k maps)
The algorithm relies on accurate feature detection but is rather runtime efficient
Lange et al., Bioinformatics (2007), 23:i273-i281

## Slide 51: Multiple Alignment
Map 1
Map 2
Map k
…
rt
m/z
T1
T2
Tk
Consensus map
Dewarp k maps onto a comparable coordinate system
Choose one map (usually the one with the largest number of features) as reference map (here: map 2 -> T2 = 1)
…
rt

## Slide 52: Quantification Strategies
Bantscheff et al., Anal Bioanal Chem (2005), 389, 1017-1031.
Common quantitative mass spectrometry workflows. Boxes in blue and yellow represent two experimental conditions. Horizontal lines indicate when samples are combined. Dashed lines indicate points at which experimental variation and thus quantification errors can occur.
Notes: ?? Was soll die hier?

## Slide 53: Materials
Quantification in general:
  Bantscheff et al., Quantitative mass spectrometry in proteomics: a critical review, Anal Bioanal Chem (2005), 389, 1017-1031 [PMID: 17668192]
Experimental methods
  SILAC: Ong, Mann, Nat Prot 1 (2007), 2650-2660.
  iTRAQ: Ross et al., Mol Cell Prot (2004), 3, 1154-1169.
Pose clustering algorithm
  Lange et al., A geometric approach for the alignment of liquid-chromatography—mass spectrometry data, Bioinformatics (2007), 23:i273-i281 [PMID: 17646306]
Nonlinear alignment
  Podwojski et al., Retention time alignment algorithms for LC/MS data must consider non-linear shifts, Bioinformatics (2009), 25 (6): 758-764. [PMID: 19176558]

## Slide 54: Materials
Online Materials
  Learning Unit 4[A,B,C]
Background
  Chromatography: Learning Unit 2A
  Statistical concepts: Learning Unit 3A