## Slide 1: Mobile Communications Chapter 2: Wireless Transmission
Frequencies
Signals, antennas, signal propagation, MIMO
Multiplexing, Cognitive Radio
Spread spectrum, modulation
Cellular systems

## Slide 2: Frequencies for communication
VLF = Very Low Frequency UHF = Ultra High Frequency
LF = Low Frequency SHF = Super High Frequency
MF = Medium Frequency EHF = Extra High Frequency
HF = High Frequency UV = Ultraviolet Light
VHF = Very High Frequency
Frequency and wave length
   = c/f
  wave length , speed of light c  3x108m/s, frequency f
1 Mm
300 Hz
10 km
30 kHz
100 m
3 MHz
1 m
300 MHz
10 mm
30 GHz
100 m
3 THz
1 m
300 THz
visible light
VLF
LF
MF
HF
VHF
UHF
SHF
EHF
infrared
UV
optical transmission
coax cable
twisted pair

## Slide 3: Example frequencies for mobile communication
VHF-/UHF-ranges for mobile radio
  simple, small antenna for cars
  deterministic propagation characteristics, reliable connections
SHF and higher for directed radio links, satellite communication
  small antenna, beam forming
  large bandwidth available
Wireless LANs use frequencies in UHF to SHF range
  some systems planned up to EHF
  limitations due to absorption by, e.g., water (dielectric heating, see microwave oven)
    weather dependent fading, signal loss caused by heavy rainfall etc.

## Slide 4: Frequencies and regulations
Examples | Europe | USA | Japan
Cellular networks | GSM 880-915, 925-960, 1710-1785, 1805-1880 UMTS 1920-1980, 2110-2170 LTE 791-821, 832-862, 2500-2690 | AMPS, TDMA, CDMA, GSM 824-849, 869-894 TDMA, CDMA, GSM, UMTS 1850-1910, 1930-1990 | PDC, FOMA 810-888, 893-958 PDC 1429-1453, 1477-1501 FOMA 1920-1980, 2110-2170
Cordless phones | CT1+ 885-887, 930-932 CT2 864-868 DECT 1880-1900 | PACS 1850-1910, 1930-1990 PACS-UB 1910-1930 | PHS 1895-1918 JCT 245-380
Wireless LANs | 802.11b/g 2412-2472 | 802.11b/g 2412-2462 | 802.11b 2412-2484 802.11g 2412-2472
Other RF systems | 27, 128, 418, 433, 868 | 315, 915 | 426, 868
In general: ITU-R holds auctions for new frequencies, manages frequency bands worldwide (WRC, World Radio Conferences); 3GPP specific: see e.g. 3GPP TS 36.101 V16.5.0 (2020-03)

## Slide 5: Great flexibility with LTE
See, e.g., en.wikipedia.org/wiki/LTE_frequency_bands or 3GPP TS 36.101 E-UTRA: User Equipment (UE) radio transmission and reception

## Slide 6: Signals I
Physical representation of data
Function of time and location
Signal parameters: parameters representing the value of data
Classification
  continuous time/discrete time
  continuous values/discrete values
  analog signal = continuous time and continuous values
  digital signal = discrete time and discrete values
Signal parameters of periodic signals:
  period T, frequency f=1/T, amplitude A, phase shift 
  sine wave as special periodic signal for a carrier: s(t) = At sin(2  ft t + t)

## Slide 7: Fourier representation of periodic signals
1
0
1
0
t
t
ideal periodic signal
real composition
(based on harmonics)

## Slide 8: Real technical systems are always bandwidth-limited
frequency [Hz]
attenuation
bandwidth
threshold
0

## Slide 9: Signals II
Different representations of signals
  amplitude (amplitude domain)
  frequency spectrum (frequency domain)
  constellation diagram (amplitude M and phase  in polar coordinates)
Composed signals transferred into frequency domain using Fourier transformation
Digital signals need
  infinite frequencies for perfect transmission
  modulation with a carrier frequency for transmission (analog signal!)
f [Hz]
A [V]

I= M cos 
Q = M sin 

A [V]
t[s]

## Slide 10: Antennas: isotropic radiator
Radiation and reception of electromagnetic waves, coupling of wires to space for radio transmission
Isotropic radiator: equal radiation in all directions (three dimensional) - only a theoretical reference antenna
Real antennas always have directive effects (vertically and/or horizontally)
Radiation pattern: measurement of radiation around an antenna
z
y
x
z
y
x
ideal
isotropic
radiator

## Slide 11: Antennas: simple dipoles
Real antennas are not isotropic radiators but, e.g., dipoles with lengths /4 on car roofs or /2 as Hertzian dipole  shape of antenna proportional to wavelength
Example: Radiation pattern of a simple Hertzian dipole
Gain: maximum power in the direction of the main lobe compared to the power of an isotropic radiator (with the same average power)
side view (xy-plane)
x
y
side view (yz-plane)
z
y
top view (xz-plane)
x
z
simple
dipole
/4
/2

## Slide 12: Antennas: directed and sectorized
Often used for microwave connections or base stations for mobile phones (e.g., radio coverage of a valley)
side view (xy-plane)
x
y
side view (yz-plane)
z
y
top view (xz-plane)
x
z
top view, 3 sector
x
z
top view, 6 sector
x
z
directed
antenna
sectorized
antenna

## Slide 13: Antennas: diversity
Grouping of 2 or more antennas
  multi-element antenna arrays
Antenna diversity
  switched diversity, selection diversity
    receiver chooses antenna with largest output
  diversity combining
    combine output power to produce gain
    cophasing needed to avoid cancellation
+
/4
/2
/4
ground plane
/2
/2
+
/2

## Slide 14: MIMO
Multiple-Input Multiple-Output
  use of several antennas at receiver and transmitter
  increased data rates and transmission range without additional transmit power or bandwidth via higher spectral efficiency, higher link robustness, reduced fading
Examples
  IEEE 802.11n, LTE, HSPA+, …
Functions
  “beamforming”: emit the same signal from all antennas to maximize signal power at receiver antenna
  spatial multiplexing: split high-rate signal into multiple lower rate streams and transmit over different antennas
  diversity coding: transmit single stream over different antennas with (near) orthogonal codes
sender
receiver
t1
t2
t3
Time of flight
t2=t1+d2
t3=t1+d3
1
2
3
Sending time
1: t0
2: t0-d2
3: t0-d3

## Slide 15: Questions & Tasks
  Frequency regulations may differ between countries. Check out the regulations valid for your country (within Europe CEPT may be able to help you, https://www.cept.org/, for the US try the FCC, www.fcc.gov, for Japan ARIB, www.arib.or.jp).
  Why can waves with a very low frequency follow the earth’s surface? Why are they not used for data transmission in computer networks?
  Why does the ITU-R only regulate ‘lower’ frequencies (up to some hundred GHz) and not higher frequencies (in the THz range)?
  What are the two different approaches in regulation regarding mobile phone systems in Europe and the US? What are the consequences?
  Why is the international availability of the same ISM bands important?
  Is it possible to transmit a digital signal, e.g., coded as square wave as used inside a computer, using radio transmission without any loss? Why?
  Is a directional antenna useful for mobile phones? Why? How can the gain of an antenna be improved?
  If you are unsure about Shannon, Nyquist etc. – go back to our Computer Networks lecture and refresh your knowledge!

## Slide 16: Signal propagation ranges
Transmission range
  communication possible
  low error rate
Detection range
  detection of the signal possible
  no communication possible
Interference range
  signal may not be detected
  signal adds to the background noise
Warning: figure misleading – bizarre shaped, time-varying ranges in reality!
distance
sender
transmission
detection
interference

## Slide 17: Signal propagation
Propagation in free space always like light (straight line)
Receiving power proportional to 1/d² in vacuum – much more attenuation in real environments, e.g., d3.5…d4 (d = distance between sender and receiver)
Receiving power additionally influenced by
  fading (frequency dependent)
  shadowing
  reflection at large obstacles
  refraction depending on the density of a medium
  scattering at small obstacles
  diffraction at edges
reflection
scattering
diffraction
shadowing
refraction

## Slide 18: Real world examples
www.ihe.kit.edu/index.php

## Slide 19: Multipath propagation
Signal can take many different paths between sender and receiver due to reflection, scattering, diffraction
Time dispersion: signal is dispersed over time
  interference with “neighbor” symbols, Inter Symbol Interference (ISI)
The signal reaches a receiver directly and phase shifted
  distorted signal depending on the phases of the different parts
signal at sender
signal at receiver
LOS pulses
multipath
pulses
LOS
(line-of-sight)

## Slide 20: Effects of mobility
Channel characteristics change over time and location
  signal paths change
  different delay variations of different signal parts
  different phases of signal parts
 quick changes in the power received (short term/fast fading)
Additional changes in
  distance to sender
  obstacles further away
 slow changes in the average power received (long term/slow fading)
short term fading
long term
fading
t
power

## Slide 21: Questions & Tasks
  What are the main problems of signal propagation? Why do radio waves not always follow a straight line? Why is reflection both useful and harmful?
  Although the examples shown here reflect real world characteristics they miss several important aspects. What could it be? What else could influence signal propagation in a real world?
  Multipath propagation seems to be harmful, but where could it help? Can a system benefit from multipath propagation? How?
  Name several methods for ISI mitigation. How does ISI depend on the carrier frequency, symbol rate, and motion of sender/receiver? What are the influences of ISI on TDM schemes?
  Remember physics in high school – where did you see certain propagation patterns of waves that can lead to short term fading?
  What could a radio receiver do against fast fading or slow fading, respectively?

## Slide 22: Multiplexing
Multiplexing in 5 dimensions
  space (si)
  time (t)
  frequency (f)
  code (c)
  polarization (p)
Goal: multiple use of a shared medium
Important: guard “spaces” needed!
Space-division multiplexing (SDM)
s2
s3
s1
f
t
c
k2
k3
k4
k5
k6
k1
f
t
c
f
t
c
channels ki

## Slide 23: Frequency-division multiplexing (FDM)
Separation of the whole spectrum into smaller frequency bands
A channel gets a certain band of the spectrum for the whole time
  Examples: classical analog TV/radio
Advantages
  no dynamic coordination necessary
  works also for analog signals
Disadvantages
  waste of bandwidth if the traffic is distributed unevenly
  inflexible
k2
k3
k4
k5
k6
k1
f
t
c

## Slide 24: Time-division multiplexing (TDM)
A channel gets the whole spectrum for a certain amount of time
  Example: round-table discussions
Advantages
  only one carrier in the medium at any time
  throughput high even for many users
Disadvantages
  precise synchronization necessary
f
t
c
k2
k3
k4
k5
k6
k1

## Slide 25: Time- and frequency-division multiplexing
Combination of both methods
A channel gets a certain frequency band for a certain amount of time
  Examples: GSM, Bluetooth
Advantages
  better protection against tapping
  protection against frequency selective interference
but: precise coordination required
f
t
c
k2
k3
k4
k5
k6
k1

## Slide 26: Cognitive Radio
Typically in the form of a spectrum sensing CR
  Detect unused spectrum and share with others avoiding interference
  Choose automatically best available spectrum (intelligent form of time/frequency/space multiplexing)
Distinguish
  Primary Users (PU): users assigned to a specific spectrum by e.g. regulation
  Secondary Users (SU): users with a CR to use unused spectrum
Examples
  Reuse of (regionally) unused analog TV spectrum (aka white space)
  Temporary reuse of unused spectrum e.g. of pagers, amateur radio etc.
space mux
frequency/time mux
PU
PU
PU
PU
SU
SU
SU
SU
f
t
PU
PU
PU
PU
PU
PU
PU
SU
SU
SU
SU
SU
SU

## Slide 27: Code-division multiplexing (CDM)
Each channel has a unique code
All channels use the same spectrum at the same time
  Example: UMTS
Advantages
  bandwidth efficient
  no coordination and synchronization necessary
  good protection against interference and tapping
Disadvantages
  varying user data rates
  more complex signal regeneration
Implemented using spread spectrum technology
k2
k3
k4
k5
k6
k1
f
t
c

## Slide 28: Polarization-division multiplexing (PDM)
Each channel has a unique polarization
  by convention: electric field considered (magnetic field always at right angle to electric field)
  e.g. vertical vs. horizontal, right vs. left circular
Examples: Satellite-TV, microwave links
Advantages
  increased bandwidth (e.g. doubled in satellite dish)
  no coordination and synchronization necessary
Disadvantages
  perfect, ideal polarization not always feasible
  cross-polarization interference (one polarization leaks into another)
Source: https://www.data-alliance.net

## Slide 29: Questions & Tasks
  Look at the multiplexing examples. What are the guard “spaces” in each of the technologies?
  Find out in which regions cognitive radios can use free spectrum e.g. from unused analog TV. What do other regions do with the “old” spectrum?
  Do you know polarization from other areas?
  Do you know of other combinations of multiplexing schemes?

## Slide 30: Modulation
Digital modulation
  digital data is translated into an analog signal (baseband)
  ASK, FSK, PSK - main focus in this chapter
  differences in spectral efficiency, power efficiency, robustness
Analog modulation
  shifts center frequency of baseband signal up to the radio carrier
  Motivation
    smaller antennas (e.g., /4)
    Frequency Division Multiplexing
    medium characteristics
  Basic schemes
    Amplitude Modulation (AM)
    Frequency Modulation (FM)
    Phase Modulation (PM)

## Slide 31: Modulation and demodulation
synchronization
decision
digital
data
analog
demodulation
radio
carrier
analog
baseband
signal
101101001
radio receiver
digital
modulation
digital
data
analog
modulation
radio
carrier
analog
baseband
signal
101101001
radio transmitter

## Slide 32: Digital modulation
Modulation of digital signals known as Shift Keying
Amplitude Shift Keying (ASK):
  very simple
  low bandwidth requirements
  very susceptible to interference
Frequency Shift Keying (FSK):
  needs larger bandwidth
Phase Shift Keying (PSK):
  more complex
  robust against interference
1
0
1
t
1
0
1
t
1
0
1
t

## Slide 33: Advanced Frequency Shift Keying
Bandwidth needed for FSK depends on the distance between the carrier frequencies
Special pre-computation avoids sudden phase shifts  MSK (Minimum Shift Keying)
  bit separated into even and odd bits, the duration of each bit is doubled
  depending on the bit values (even, odd) the higher or lower frequency, original or inverted is chosen
  the frequency of one carrier is twice the frequency of the other
  Equivalent to offset QPSK
Even higher bandwidth efficiency using a Gaussian low-pass filter  GMSK (Gaussian MSK), used in GSM

## Slide 34: Example of MSK
data
even bits
odd bits
1
1
1
1
0
0
0
t
low frequency
high frequency
MSK
signal
bit
even 0 1 0 1
odd 0 0 1 1
signal h n n h value - - + +
h: high frequency
n: low frequency
+: original signal
-: inverted signal
No phase shifts!

## Slide 35: Advanced Phase Shift Keying
BPSK (Binary Phase Shift Keying):
  bit value 0: sine wave
  bit value 1: inverted sine wave
  very simple PSK
  low spectral efficiency
  robust, used e.g. in satellite systems
QPSK (Quadrature Phase Shift Keying):
  2 bits coded as one symbol
  symbol determines shift of sine wave
  needs less bandwidth compared to BPSK
  more complex
Often also transmission of relative, not absolute phase shift
  DQPSK - Differential QPSK (IS-136, PHS)
11
10
00
01
Q
I
0
1
Q
I
11
01
10
00
A
t

## Slide 36: Quadrature Amplitude Modulation
Quadrature Amplitude Modulation (QAM)
  combines amplitude and phase modulation
  it is possible to code n bits using one symbol
  2n discrete levels, n=2 identical to QPSK
Bit error rate increases with n, but less errors compared to comparable PSK schemes
  Example: 16-QAM (4 bits = 1 symbol)
  Symbols 0011 and 0001 have the same phase φ, but different amplitude a. 0000 and 1000 have different phase, but same amplitude.
0000
0001
0011
1000
Q
I
0010
φ
a

## Slide 37: Hierarchical Modulation
DVB-T modulates two separate data streams onto a single DVB-T stream
High Priority (HP) embedded within a Low Priority (LP) stream
Multi carrier system, about 2000 or 8000 carriers
QPSK, 16 QAM, 64QAM (the newer DVB-T2 can additionally use 256QAM)
Example: 64QAM
  good reception: resolve the entire 64QAM constellation
  poor reception, mobile reception: resolve only QPSK portion
  6 bit per QAM symbol, 2 most significant determine QPSK
  HP service coded in QPSK (2 bit), LP uses remaining 4 bit
Q
I
00
10
000010
010101

## Slide 38: Questions & Tasks
  Why, typically, is digital modulation not enough for radio transmission? What are general goals for digital modulation? What are typical schemes?
  Think of a phase diagram and the points representing bit patterns for a PSK scheme. How can a receiver decide which bit pattern was originally sent when a received ‘point’ lies somewhere in between other points in the diagram? Why is it, thus, difficult to code more and more bits per phase shift?
  How can a system react in case of higher/lower interference? How does this influence the data rate?

## Slide 39: Spread spectrum technology
Problem of radio transmission: frequency dependent fading can wipe out narrow band signals for duration of the interference
Solution: spread the narrow band signal into a broad band signal using a special code
  protection against narrow band interference
Side effects:
  coexistence of several signals without dynamic coordination
  tap-proof
Alternatives: Direct Sequence, Frequency Hopping
detection at
receiver
interference
spread signal
signal
spread
interference
f
f
power
power

## Slide 40: Effects of spreading and interference
dP/df
f
i)
dP/df
f
ii)
sender
dP/df
f
iii)
dP/df
f
iv)
receiver
f
v)
user signal
broadband interference
narrowband interference
dP/df

## Slide 41: Spreading and frequency selective fading
frequency
channel quality
1
2
3
4
5
6
narrow band signal
guard space
2
2
2
2
2
frequency
channel quality
1
spread spectrum
narrowband channels
spread spectrum channels

## Slide 42: DSSS (Direct Sequence Spread Spectrum) I
XOR of the signal with pseudo-random number (chipping sequence)
  many chips per bit (e.g., 128) result in higher bandwidth of the signal
Advantages
  reduces frequency selective fading
  in cellular networks
    base stations can use the same frequency range
    several base stations can detect and recover the signal
    soft handover
Disadvantages
  precise power control necessary
user data
chipping
sequence
resulting
signal
0
1
0
1
1
0
1
0
1
0
1
0
0
1
1
1
XOR
0
1
1
0
0
1
0
1
1
0
1
0
0
1
=
tb
tc
tb: bit period
tc: chip period

## Slide 43: DSSS (Direct Sequence Spread Spectrum) II
X
user data
chipping
sequence
modulator
radio
carrier
spread
spectrum
signal
transmitted
signal
transmitter
demodulator
received
signal
radio
carrier
X
chipping
sequence
lowpass
filtered
signal
receiver
integrator
products
decision
data
sampled
sums
correlator

## Slide 44: FHSS (Frequency Hopping Spread Spectrum) I
Discrete changes of carrier frequency
  sequence of frequency changes determined via pseudo random number sequence
Two versions
  Fast Hopping: several frequencies per user bit
  Slow Hopping: several user bits per frequency
Advantages
  frequency selective fading and interference limited to short period
  simple implementation
  uses only small portion of spectrum at any time
Disadvantages
  not as robust as DSSS
  simpler to detect

## Slide 45: FHSS (Frequency Hopping Spread Spectrum) II
user data
slow
hopping
(3 bits/hop)
fast
hopping
(3 hops/bit)
0
1
tb
0
1
1
t
f
f1
f2
f3
t
td
f
f1
f2
f3
t
td
tb: bit period td: dwell time

## Slide 46: FHSS (Frequency Hopping Spread Spectrum) III
modulator
user data
hopping
sequence
modulator
narrowband
signal
spread
transmit
signal
transmitter
received
signal
receiver
demodulator
data
frequency
synthesizer
hopping
sequence
demodulator
frequency
synthesizer
narrowband
signal

## Slide 47: Software Defined Radio
Basic idea (ideal world)
  Full flexibility wrt. modulation, carrier frequency, coding…
  Simply download a new radio!
  Transmitter: digital signal processor plus very fast D/A-converter
  Receiver: very fast A/D-converter plus digital signal processor
Real world
  Problems due to interference, high accuracy/high data rate, low-noise amplifiers needed, filters etc.
Examples
  Joint Tactical Radio System, GNU Radio, Universal Software Radio Peripheral, …
  see e.g. SDR – 20 Years Later, IEEE Communications Magazine, Sept. 2015 and Jan. 2016
Application
Signal Processor
D/A Converter
Application
Signal Processor
A/D Converter

## Slide 48: Questions & Tasks
  What are the means to mitigate narrowband interference? What is the complexity of the different solutions?
  What are the main benefits of a spread spectrum system? How can spreading be achieved?
  What replaces the guard space in FDM when compared to CDM?
  How can DSSS systems benefit from multipath propagation?
  Look-up the developments of SDRs today. What can be done already with low-cost SDRs? (see e.g. GNU radio, https://www.gnuradio.org/)

## Slide 49: Cell structure
Implements space division multiplex
  base station covers a certain transmission area (cell)
Mobile stations communicate only via the base station
Advantages of cell structures
  higher capacity, higher number of users
  less transmission power needed
  more robust, decentralized
  base station deals with interference, transmission area etc. locally
Problems
  fixed network needed for the base stations
  handover (changing from one cell to another) necessary
  interference with other cells
Cell sizes from some 100 m in cities to, e.g., 35 km on the country side (GSM) - even less for higher frequencies

## Slide 50: Frequency planning I
Frequency reuse only with a certain distance between the base stations
Standard model using 7 frequencies:
Fixed frequency assignment:
  certain frequencies are assigned to a certain cell
  problem: different traffic load in different cells
Dynamic frequency assignment:
  base station chooses frequencies depending on the frequencies already used in neighbor cells
  more capacity in cells with more traffic
  assignment can also be based on interference measurements
f4
f5
f1
f3
f2
f6
f7
f3
f2
f4
f5
f1

## Slide 51: Frequency planning II
f1
f2
f3
f2
f1
f1
f2
f3
f2
f3
f1
f2
f1
f3
f3
f3
f3
f3
f4
f5
f1
f3
f2
f6
f7
f3
f2
f4
f5
f1
f3
f5
f6
f7
f2
f2
f1
f1
f1
f2
f3
f2
f3
f2
f3
h1
h2
h3
g1
g2
g3
h1
h2
h3
g1
g2
g3
g1
g2
g3
3 cell cluster
7 cell cluster
3 cell cluster
with 3 sector antennas

## Slide 52: Cell breathing
CDM systems: cell size depends on current load
Additional traffic appears as noise to other users
If the noise level is too high users drop out of cells

## Slide 53: Questions & Tasks
  What are the main reasons for using cellular systems? How is SDM typically realized and combined with FDM? How does dynamic frequency assignment influence the frequencies available in other cells?
  What limits the number of simultaneous users in a TDM/FDM system compared to a CDM system? What happens to the transmission quality of connections if the load gets higher in a cell, i.e., how does an additional user influence the other users in the cell?