## Slide 1: Mobile Communications Chapter 4: Wireless Telecommunication Systems
Market
GSM
TETRA
UMTS/IMT-2000
LTE/LTE advanced

## Slide 2: Mobile phone subscribers worldwide (we were all wrong)
year
Subscribers [million]
0
200
400
600
800
1000
1200
1400
1600
1996
1997
1998
1999
2000
2001
2002
2003
2004
approx. 1.7 bn
GSM total
TDMA total
CDMA total
PDC total
Analogue total
W-CDMA
Total wireless
Prediction (1998)
2016: 7.8 bn total
4.7 bn unique human
4.7% growth/year

## Slide 3: Some current numbers (2019/2020)
Source: GSMAIntelligence
Source: statista
Source: statista

## Slide 4: World largest mobile network operators 2019
Source: The Daily Records
Chart: 
 | 874
 | 516
 | 403
 | 301
 | 280
 | 273
 | 270
 | 255
 | 238
 | 172
2014: $10.25 ARPU/month
However: -2.8% growth/year
2018: $8.45 ARPU/month
-0.8% growth/year

## Slide 5: Development of mobile telecommunication systems
1G
2G
3G
2.5G
IS-95
cdmaOne
IS-136
TDMA
D-AMPS
GSM
PDC
GPRS
IMT-DS
UTRA FDD / W-CDMA
EDGE
IMT-TC
UTRA TDD / TD-CDMA
cdma2000 1X
1X EV-DV
(3X)
AMPS
NMT
IMT-SC
IS-136HS
UWC-136
IMT-TC
TD-SCDMA
CT0/1
CT2
IMT-FT
DECT
CDMA
TDMA
FDMA
IMT-MC
cdma2000 1X EV-DO
HSPA
3.9G
4G
LTE
LTE
advanced
5G
New Radio
+ OFDM
+ beamforming
2.75G

## Slide 6: Some press news…
16th April 2008: The GSMA, the global trade group for the mobile industry, today announced that total connections to GSM mobile communications networks have now passed the 3 Billion mark globally. The third billion landmark has been reached just four years after the GSM industry surpassed its first billion, and just two years from the second billionth connection. The 3 Billion landmark has been surpassed just 17 years after the first GSM network launch in 1991. Today more than 700 mobile operators across 218 countries and territories of the world are adding new connections at the rate of 15 per second, or 1.3 million per day.
11 February 2009: The GSMA today announced that the mobile world has celebrated its four billionth connection, according to Wireless Intelligence, the GSMA’s market intelligence unit. This milestone underscores the continued strong growth of the mobile industry and puts the global market on the path to reach a staggering six billion connections by 2013.
By 2014 3.4bn people have broadband, 80% mobile!
2018: more than 8.5 billion mobile connections, more than 5 billion unique subscribers, $9,49 ARPU/month (https://www.gsmaintelligence.com/)
2020: 5G networks and phones start spreading worldwide

## Slide 7: How does it work?
How can the system locate a user?
Why don’t all phones ring at the same time?
What happens if two users talk simultaneously?
Why don’t I get the bill from my neighbor?
Why can an Australian use her phone in Berlin?
Why can’t I simply overhear the neighbor’s communication?
How secure is the mobile phone system?
What are the key components of the mobile phone network?

## Slide 8: Questions & Tasks
  Why do we have so many more connections compared to subscribers?
  Who/what is driving mobile communications in the future?
  What are consequences of a shrinking ARPU? What can companies do?
  Who defines the generations of mobile telecommunication systems?
  Visit some of the statistics pages and check-out the newest numbers!
  Go through the simple questions and keep them in mind. These are the questions you definitively have to able to answer after this chapter for all systems presented!

## Slide 9: GSM – the most successful 2G system: Overview
GSM
    formerly: Groupe Spéciale Mobile (founded 1982)
    now: Global System for Mobile Communication
    Pan-European standard (ETSI, European Telecommunications Standardisation Institute)
    simultaneous introduction of essential services in three phases (1991, 1994, 1996) by the European telecommunication administrations (Germany: D1 and D2)  seamless roaming within Europe possible
2008: many providers all over the world use GSM (almost all countries in Asia, Africa, Europe, Australia, America)
    more than 4.2 billion subscribers in more than 700 networks
    more than 75% of all digital mobile phones use GSM
    over 29 billion SMS in Germany in 2008 (> 10% of the revenues for many operators) [be aware: these are only rough numbers…]

## Slide 10: Good bye SMS!?

## Slide 11: Performance characteristics of GSM (wrt. analog sys.)
Communication
    mobile, wireless communication; support for voice and data services
Total mobility
    international access, chip-card enables use of access points of different providers
Worldwide connectivity
    one number, the network handles localization
High capacity
    better frequency efficiency, smaller cells, more customers per cell
High transmission quality
    high audio quality and reliability for wireless, uninterrupted phone calls at higher speeds (e.g., from cars, trains)
Security functions
    access control, authentication via chip-card and PIN

## Slide 12: Disadvantages of GSM
There is no perfect system!!
  no end-to-end encryption of user data
  no full ISDN bandwidth of 64 kbit/s to the user, no transparent B-channel
  reduced concentration while driving
  electromagnetic radiation
  abuse of private data possible
  roaming profiles accessible
  high complexity of the system
  several optional capabilities within the GSM standards

## Slide 13: GSM: Mobile Services
GSM offers
    several types of connections
    voice connections, data connections, short message service
    multi-service options (combination of basic services)
Three service domains
    Bearer Services
    Telematic Services
    Supplementary Services
GSM-PLMN
transit
network
(PSTN, ISDN)
source/
destination
network
TE
TE
bearer services
telematic services
R, S
(U, S, R)
Um
MT
MS

## Slide 14: Bearer Services
Telecommunication services to transfer data between access points
Specification of services up to the terminal interface (OSI layers 1-3)
Different data rates for voice and data (original standard)
    data service (circuit switched)
        synchronous: 2.4, 4.8 or 9.6 kbit/s
        asynchronous: 300 - 1200 bit/s
    data service (packet switched)
        synchronous: 2.4, 4.8 or 9.6 kbit/s
        asynchronous: 300 - 9600 bit/s
Today (classical GSM!):
    data rates of approx. 50 kbit/s possible – will be covered later!
    far more with new modulation scheme

## Slide 15: Tele Services I
Telecommunication services that enable voice communication via mobile phones
All these basic services have to obey cellular functions, security measurements etc.
Offered services
    mobile telephony
        primary goal of GSM was to enable mobile telephony offering the traditional bandwidth of 3.1 kHz
    emergency number
        common number throughout Europe (112)
        mandatory for all service providers
        free of charge
        connection with the highest priority (preemption of other connections possible)
    multi-numbering
        several ISDN phone numbers per user possible

## Slide 16: Tele Services II
Additional services
    Non-Voice-Teleservices
        group 3 fax
        voice mailbox (implemented in the fixed network supporting the mobile terminals)
        electronic mail (MHS, Message Handling System, implemented in the fixed network)
        ...
    Short Message Service (SMS)
        alphanumeric data transmission to/from the mobile terminal (160 characters) using the signaling channel, thus allowing simultaneous use of basic services and SMS
        almost ignored in the beginning then the most successful add-on!
            but more and more replaced by IP-based messaging

## Slide 17: Supplementary services
Services in addition to the basic services, cannot be offered stand-alone
Similar to ISDN services besides lower bandwidth due to the radio link
May differ between different service providers, countries and protocol versions
Important services
    identification: forwarding of caller number
    suppression of number forwarding
    automatic call-back
    conferencing with up to 7 participants
    locking of the mobile terminal (incoming or outgoing calls)
    ...

## Slide 18: Questions & Tasks
  What is SMS still used for? What do the replacements require?
  Why was GSM such a big success?
  What are the main differences between GSM and ISDN (at a high level)?
  What is required in the background of 112?
  Look at the characteristics of GSM and its disadvantages. What has changed, what is the same if you compare GSM with today’s systems?

## Slide 19: Architecture of the GSM system
GSM is a PLMN (Public Land Mobile Network)
    several providers setup mobile networks following the GSM standard within each country
    components
        MS (mobile station)
        BS (base station)
        MSC (mobile switching center)
        LR (location register)
    subsystems
        RSS (radio subsystem): covers all radio aspects
        NSS (network and switching subsystem): call forwarding, handover, switching
        OSS (operation subsystem): management of the network

## Slide 20: Ingredients 1: Mobile Phones, Smartphones & Co.
The visible but smallest
part of the network!
Source: Time Magazine, 09/14
Source: Tech Best, https://www.youtube.com/watch?v=g7i00InEzhI
Source: www.riot-os.org

## Slide 21: Ingredients 2: Antennas
Still visible – cause many discussions…

## Slide 22: Ingredients 3: Infrastructure 1
Base Stations
Cabling
Microwave links

## Slide 23: Ingredients 3: Infrastructure 2
Switching units
Data bases
Management
Monitoring
Not „visible“, but comprise the major part of the network (also from an investment point of view…)

## Slide 24: GSM: overview
fixed network
BSC
BSC
MSC
MSC
GMSC
OMC, EIR, AUC
VLR
HLR
NSS
with OSS
RSS
VLR

## Slide 25: GSM: elements and interfaces
NSS
MS
MS
BTS
BSC
GMSC
IWF
OMC
BTS
BSC
MSC
MSC
Abis
Um
EIR
HLR
VLR
VLR
A
BSS
PDN
ISDN, PSTN
RSS
radio cell
radio cell
MS
AUC
OSS
signaling
O

## Slide 26: GSM: system architecture
Um
Abis
A
BSS
radio subsystem
MS
MS
BTS
BSC
BTS
BTS
BSC
BTS
network and switching subsystem
MSC
MSC
fixed partner networks
IWF
ISDN PSTN
PSPDN CSPDN
SS7
EIR
HLR
VLR
ISDN PSTN

## Slide 27: System architecture: radio subsystem
Components
  MS (Mobile Station)
  BSS (Base Station Subsystem): consisting of
    BTS (Base Transceiver Station): sender and receiver
    BSC (Base Station Controller): controlling several transceivers
Interfaces
  Um : radio interface
  Abis : standardized, open interface with 16 kbit/s user channels
  A: standardized, open interface with 64 kbit/s user channels
Um
Abis
A
BSS
radio subsystem
network and switching subsystem
MS
MS
BTS
BSC
MSC
BTS
BTS
BSC
BTS
MSC

## Slide 28: System architecture: network and switching subsystem
Components
  MSC (Mobile Services Switching Center):
  IWF (Interworking Functions)
  ISDN (Integrated Services Digital Network)
  PSTN (Public Switched Telephone Network)
  PSPDN (Packet Switched Public Data Net.)
  CSPDN (Circuit Switched Public Data Net.)
Databases
  HLR (Home Location Register)
  VLR (Visitor Location Register)
  EIR (Equipment Identity Register)
network subsystem
MSC
MSC
fixed partner networks
IWF
ISDN PSTN
PSPDN CSPDN
SS7
EIR
HLR
VLR
ISDN PSTN

## Slide 29: Radio subsystem
The Radio Subsystem (RSS) comprises the cellular mobile network up to the switching centers
Components
  Base Station Subsystem (BSS):
    Base Transceiver Station (BTS): radio components including sender, receiver, antenna - if directed antennas are used one BTS can cover several cells
    Base Station Controller (BSC): switching between BTSs, controlling BTSs, managing of network resources, mapping of radio channels (Um) onto terrestrial channels (A interface)
    BSS = BSC + sum(BTS) + interconnection
  Mobile Stations (MS)

## Slide 30: GSM: cellular network
use of several carrier frequencies
not the same frequency in adjoining cells
cell sizes vary from some 100 m up to 35 km depending on user density, geography, transceiver power etc.
hexagonal shape of cells is idealized (cells overlap, shapes depend on geography)
if a mobile user changes cells handover of the connection to the neighbor cell
possible radio coverage of the cell
idealized shape of the cell
cell
segmentation of the area into cells

## Slide 31: GSM frequency bands (examples)
Type | Channels | Uplink [MHz] | Downlink [MHz]
GSM 850 | 128-251 | 824-849 | 869-894
GSM 900 classical extended | 0-124, 955-1023 124 channels +49 channels | 876-915 890-915 880-915 | 921-960 935-960 925-960
GSM 1800 | 512-885 | 1710-1785 | 1805-1880
GSM 1900 | 512-810 | 1850-1910 | 1930-1990
GSM-R exclusive | 955-1024, 0-124 69 channels | 876-915 876-880 | 921-960 921-925
Additionally: GSM 400 (also named GSM 450 or GSM 480 at 450-458/460-468 or 479-486/489-496 MHz)
Please note: frequency ranges may vary depending on the country!
Channels at the lower/upper edge of a frequency band are typically not used

## Slide 32: Example coverage of GSM networks (historical from www.gsmworld.com)
T-Mobile (GSM-900/1800) Germany
O2 (GSM-1800) Germany
AT&T (GSM-850/1900) USA
Vodacom (GSM-900) South Africa

## Slide 33: Base Transceiver Station and Base Station Controller
Tasks of a BSS are distributed over BSC and BTS
BTS comprises radio specific functions
BSC is the switching center for radio channels

## Slide 34: Mobile station
Terminal for the use of GSM services
A mobile station (MS) comprises several functional groups
  MT (Mobile Terminal):
    offers common functions used by all services the MS offers
    corresponds to the network termination (NT) of an ISDN access
    end-point of the radio interface (Um)
  TA (Terminal Adapter):
    terminal adaptation, hides radio specific characteristics
  TE (Terminal Equipment):
    peripheral device of the MS, offers services to a user
    does not contain GSM specific functions
  SIM (Subscriber Identity Module):
    personalization of the mobile terminal, stores user parameters – more and more replaced by eSIM
R
S
Um
TE
TA
MT
Source: geektrooper.wordpress.com

## Slide 35: Network and switching subsystem
NSS is the main component of the public mobile network GSM
  switching, mobility management, interconnection to other networks, system control
Components
  Mobile Services Switching Center (MSC) controls all connections via a separated network to/from a mobile terminal within the domain of the MSC - several BSC can belong to a MSC
  Databases (important: scalability, high capacity, low delay)
    Home Location Register (HLR) central master database containing user data, permanent and semi-permanent data of all subscribers assigned to the HLR (one provider can have several HLRs)
    Visitor Location Register (VLR) local database for a subset of user data, including data about all user currently in the domain of the VLR

## Slide 36: Mobile Services Switching Center
The MSC (mobile services switching center) plays a central role in GSM
  switching functions
  additional functions for mobility support
  management of network resources
  interworking functions via Gateway MSC (GMSC)
  integration of several databases
Functions of an MSC
  specific functions for paging and call forwarding
  termination of SS7 (signaling system no. 7)
  mobility specific signaling
  location registration and forwarding of location information
  provision of new services (fax, data calls)
  support of short message service (SMS)
  generation and forwarding of accounting and billing information

## Slide 37: Operation subsystem
The OSS (Operation Subsystem) enables centralized operation, management, and maintenance of all GSM subsystems
Components
  Authentication Center (AUC)
    generates user specific authentication parameters on request of a VLR
    authentication parameters used for authentication of mobile terminals and encryption of user data on the air interface within the GSM system
  Equipment Identity Register (EIR)
    registers GSM mobile stations and user rights
    stolen or malfunctioning mobile stations can be locked and sometimes even localized
  Operation and Maintenance Center (OMC)
    different control capabilities for the radio subsystem and the network subsystem

## Slide 38: Questions & Tasks
  You should be able to draw the architecture of the classical GSM system and to describe the functionality of the components!
  What are the advantages of specifying not only the radio interface but also all internal interfaces of the GSM system?
  Could there be a single point of failure in the GSM architecture? How to avoid it?
  In which database is a roaming tourist registered?
  How could the system block all stolen GSM phones?
  How can the system localizes mobile phones (at least to a certain precision…)?
  Why does GSM separate the MS and SIM?
  What is the advantage/disadvantage of an eSIM?

## Slide 39: GSM - TDMA/FDMA
1
2
3
4
5
6
7
8
higher GSM frame structures
935-960 MHz
124 channels (200 kHz)
downlink
890-915 MHz
124 channels (200 kHz)
uplink
frequency
time
GSM TDMA frame
GSM time-slot (normal burst)
4.615 ms
546.5 µs
577 µs
tail
user data
Training
S
guard
space
S
user data
tail
guard
space
3 bits
57 bits
26 bits
57 bits
1
1
3

## Slide 40: GSM hierarchy of frames
0
1
2
2045
2046
2047
...
hyperframe
0
1
2
48
49
50
...
0
1
24
25
...
superframe
0
1
24
25
...
0
1
2
48
49
50
...
0
1
6
7
...
multiframe
frame
burst
slot
577 µs
4.615 ms
120 ms
235.4 ms
6.12 s
3 h 28 min 53.76 s

## Slide 41: GSM protocol layers for signaling
CM
MM
RR
MM
LAPDm
radio
LAPDm
radio
LAPD
PCM
RR’
BTSM
CM
LAPD
PCM
RR’
BTSM
16/64 kbit/s
Um
Abis
A
SS7
PCM
SS7
PCM
64 kbit/s /
2.048 Mbit/s
MS
BTS
BSC
MSC
BSSAP
BSSAP

## Slide 42: Questions & Tasks
  Go once more through the channel/slot structure and understand where GSM applies what type of multiplexing!
  How does GSM adapt to varying distances between MS and BTS? What is the role of the guard spaces?
  What limits the radius of a GSM cell?
  What is the maximum data rate per time slot? Why is the real data rate offered that much lower?

## Slide 43: Mobile Terminated Call
1: calling a GSM subscriber
2: forwarding call to GMSC
3: signal call setup to HLR
4, 5: request MSRN from VLR
6: forward responsible MSC to GMSC
7: forward call to
current MSC
8, 9: get current status of MS
10, 11: paging of MS
12, 13: MS answers
14, 15: security checks
16, 17: set up connection
PSTN
calling
station
GMSC
HLR
VLR
BSS
BSS
BSS
MSC
MS
1
2
3
4
5
6
7
8
9
10
11
12
13
16
10
10
11
11
11
14
15
17

## Slide 44: Mobile Originated Call
1, 2: connection request
3, 4: security check
5-8: check resources (free circuit)
9-10: set up call
PSTN
GMSC
VLR
BSS
MSC
MS
1
2
6
5
3
4
9
10
7
8

## Slide 45: MTC/MOC
BTS
MS
paging request
channel request
immediate assignment
paging response
authentication request
authentication response
ciphering command
ciphering complete
setup
call confirmed
assignment command
assignment complete
alerting
connect
connect acknowledge
data/speech exchange
BTS
MS
channel request
immediate assignment
service request
authentication request
authentication response
ciphering command
ciphering complete
setup
call confirmed
assignment command
assignment complete
alerting
connect
connect acknowledge
data/speech exchange
MTC
MOC

## Slide 46: 4 types of handover
MSC
MSC
BSC
BSC
BSC
BTS
BTS
BTS
BTS
MS
MS
MS
MS
1
2
3
4

## Slide 47: Handover decision
receive level
BTSold
receive level
BTSnew
MS
MS
HO_MARGIN
BTSold
BTSnew

## Slide 48: Handover procedure
HO access
BTSold
BSCnew
measurement
result
BSCold
Link establishment
MSC
MS
measurement
report
HO decision
HO required
BTSnew
HO request
resource allocation
ch. activation
ch. activation ack
HO request ack
HO command
HO command
HO command
HO complete
HO complete
clear command
clear command
clear complete
clear complete
Hard handover

## Slide 49: Questions & Tasks
  How does the GSM system locate an MS? How precise is the localization?
  Why does the system use a handover margin?
  Why is the hand over called “hard”?
  How and where is user-related data represented/stored in the GSM system?

## Slide 50: Security in GSM
Security services
  access control/authentication
    user  SIM (Subscriber Identity Module): secret PIN (personal identification number)
    SIM  network: challenge response method
  confidentiality
    voice and signaling encrypted on the wireless link (after successful authentication)
  anonymity
    temporary identity TMSI (Temporary Mobile Subscriber Identity)
    newly assigned at each new location update (LUP)
    encrypted transmission
3 algorithms specified in GSM
  A3 for authentication (“secret”, open interface)
  A5 for encryption (standardized)
  A8 for key generation (“secret”, open interface)
“secret”:
A3 and A8 available via the Internet
network providers can (and do) use stronger mechanisms

## Slide 51: GSM - authentication
A3
RAND
Ki
128 bit
128 bit
SRES* 32 bit
A3
RAND
Ki
128 bit
128 bit
SRES 32 bit
SRES* =? SRES
SRES
RAND
SRES
32 bit
mobile network
SIM
AC
MSC
SIM
Ki: individual subscriber authentication key SRES: signed response

## Slide 52: GSM - key generation and encryption
A8
RAND
Ki
128 bit
128 bit
Kc
64 bit
A8
RAND
Ki
128 bit
128 bit
SRES
RAND
encrypted data
mobile network (BTS)
MS with SIM
AC
BSS
SIM
A5
Kc
64 bit
A5
MS
data
data
cipher
key

## Slide 53: Questions & Tasks
  What is protected by the GSM security mechanisms?
  What is missing compared to today’s communication systems?
  What are reasons for this decision?

## Slide 54: Data services in GSM I
Data transmission standardized with only 9.6 kbit/s
  advanced coding allows 14.4 kbit/s
  not enough for Internet and multimedia applications
HSCSD (High-Speed Circuit Switched Data)
  mainly software update
  bundling of several time-slots to get higher AIUR (Air Interface User Rate, e.g., 57.6 kbit/s using 4 slots @ 14.4)
  advantage: ready to use, constant quality, simple
  disadvantage: channels blocked for voice transmission

## Slide 55: Data services in GSM II
GPRS (General Packet Radio Service)
  packet switching
  using free slots only if data packets ready to send (e.g., 50 kbit/s using 4 slots temporarily)
  standardization 1998, introduction 2001
  advantage: one step towards UMTS, more flexible
  disadvantage: more investment needed (new hardware)
GPRS network elements
  GSN (GPRS Support Nodes): GGSN and SGSN
  GGSN (Gateway GSN)
    interworking unit between GPRS and PDN (Packet Data Network)
  SGSN (Serving GSN)
    supports the MS (location, billing, security)
  GR (GPRS Register)
    user addresses

## Slide 56: GPRS quality of service

## Slide 57: Examples for GPRS device classes
Class | Receiving slots | Sending slots | Maximum number of slots
1 | 1 | 1 | 2
2 | 2 | 1 | 3
3 | 2 | 2 | 3
5 | 2 | 2 | 4
8 | 4 | 1 | 5
10 | 4 | 2 | 5
12 | 4 | 4 | 5

## Slide 58: GPRS user data rates in kbit/s
Coding scheme | 1 slot | 2 slots | 3 slots | 4 slots | 5 slots | 6 slots | 7 slots | 8 slots
CS-1 | 9.05 | 18.1 | 27.15 | 36.2 | 45.25 | 54.3 | 63.35 | 72.4
CS-2 | 13.4 | 26.8 | 40.2 | 53.6 | 67 | 80.4 | 93.8 | 107.2
CS-3 | 15.6 | 31.2 | 46.8 | 62.4 | 78 | 93.6 | 109.2 | 124.8
CS-4 | 21.4 | 42.8 | 64.2 | 85.6 | 107 | 128.4 | 149.8 | 171.2

## Slide 59: GPRS architecture and interfaces
MS
BSS
GGSN
SGSN
MSC
Um
EIR
HLR/
GR
VLR
PDN
Gb
Gn
Gi
SGSN
Gn

## Slide 60: GPRS protocol architecture
apps.
IP/X.25
LLC
GTP
MAC
radio
MAC
radio
FR
RLC
BSSGP
IP/X.25
FR
Um
Gb
Gn
L1/L2
L1/L2
MS
BSS
SGSN
GGSN
UDP/TCP
Gi
SNDCP
RLC
BSSGP
IP
IP
LLC
UDP/TCP
SNDCP
GTP

## Slide 61: Questions & Tasks
  What multiplexing schemes are used in GSM for what purposes? Think also of other layers apart from the physical layer.
  How is synchronisation achieved in GSM? Who is responsible for synchronisation and why is synchronisation very important?
  How is the shift from voice-only to Internet-style traffic reflected in the GSM system?
  Why is a new infrastructure needed for GPRS, but not for HSCSD? Which components are new and what is their purpose?
  Only few operators offered HSCSD – why?
  What are the reasons for the delays in a GSM system for packet data traffic? Distinguish between circuit-switched and packet-switched transmission.
  Relatively high delay, low reliability – why was GPRS yet a break-through in the GSM world?
  What are the limitations of a GSM cell in terms of diameter and capacity (voice, data) for the traditional GSM, HSCSD, GPRS? How can the capacity be increased?
  What determines the coding scheme?
  Give reasons for a handover in GSM and the problems associated with it. Which are the typical steps for handover, what types of handover can occur? Which resources need to be allocated during handover for data transmission using HSCSD or GPRS respectively? What about QoS guarantees?

## Slide 62: TETRA - Terrestrial Trunked Radio
Trunked radio systems
  many different radio carriers
  assign single carrier for a short period to one user/group of users
  taxi service, fleet management, rescue teams
  interfaces to public networks, voice and data services
  very reliable, fast call setup, local operation
TETRA - ETSI standard, 2G system, EN 300 392
  formerly: Trans European Trunked Radio
    https://www.etsi.org/technologies/tetra
  point-to-point and point-to-multipoint
  encryption (end-to-end, air interface), authentication of devices, users and networks
  group call, broadcast, sub-second group-call setup
  ad-hoc (“direct mode”), relay and infrastructure networks
  call queuing with pre-emptive priorities
  Push-To-Talk (PTT)
Source: www.motorolasolutions.com
Source: www.sepura.com
Source: tcca.info

## Slide 63: TETRA – Markets by sector
Source: www.grandviewresearch.com
Estimated 5 mio. terminals in 2020
Used in over 120 countries

## Slide 64: TETRA – Network Architecture
TETRA infrastructure
BS
BS
switch
switch
switch
NMS
BS
other TETRA networks
PSTN, ISDN,
Internet, PDN
DMO
ISI
PEI
AI
AI: Air Interface
BS: Base Station
DMO: Direct Mode Operation
ISI: Inter-System Interface
NMS: Network Management
System
PEI: Peripheral Equipment
Interface

## Slide 65: TETRA – Direct Mode I
Direct Mode enables ad-hoc operation and is one of the most important differences to pure infrastructure-based networks such as GSM, cdma2000 or UMTS.
Individual Call
Group Call
“Dual Watch” – alternating participation in
Infrastructure and ad-hoc
network
Managed Direct Mode
network
Authorizing
mobile station

## Slide 66: TETRA – Direct Mode II
An additional repeater may increase the transmission range (e.g. police car)
Direct Mode with Gateway
network
Direct Mode with Repeater
Direct Mode with Repeater/Gateway
network
Managed Repeater/Gateway
network
Authorizing
Repeater

## Slide 67: TETRA – Technology
Services
  Voice+Data (V+D) and Packet Data Optimized (PDO)
  Short data service (SDS)
Frequencies
  Duplex: FDD, Modulation: DQPSK
  Europe (in MHz, not all available yet)
    380-390 UL / 390-400 DL; 410-420 UL / 420-430 DL, 450-460 UL / 460-470 DL; 870-876 UL / 915-921 DL
  Other countries
    380-390 UL / 390-400 DL; 410-420 UL / 420-430 DL, 806-821 UL / 851-866 DL

## Slide 68: TDMA structure of the voice+data system
0
1
2
57
58
59
...
hyperframe
0
1
2
15
16
17
...
multiframe
0
1
2
3
0 slot 509
frame
14.17 ms
56.67 ms
1.02 s
61.2 s
CF
Control Frame

## Slide 69: TETRA – Data Rates
Infrastructure mode, V+D in kbit/s
No. of time slots 1 2 3 4
No protection 7.2 14.4 21.6 28.8
Low protection 4.8 9.6 14.4 19.2
High protection 2.4 4.8 7.2 9.6
TETRA Release 2 – Supporting higher data rates
  TEDS (TETRA Enhanced Data Service)
  up to 100-500 kbit/s
    depends on modulation (DQPSK, D8PSK, 4/16/64QAM) and channel width (25/50/100/150 kHz)
  backward compatibility
Future of TETRA?
Data rates to low compared to e.g. LTE
Specialized devices very expensive (no COTS)
LTE Public Safety Broadband

## Slide 70: Questions & Tasks
  Why using a separated, specialized system like TETRA? Why not using the “normal” cellular phone network with some “extras”? There are reasons for and against such an approach!
  What else could be problematic using e.g. current LTE/UMTS/GSM systems?
  Check the current approaches of 3GPP towards a public safety mobile network! What is a general trend?

## Slide 71: UMTS and IMT-2000 – The 3rd Generation
Proposals for IMT-2000 (International Mobile Telecommunications)
  UWC-136, cdma2000, WP-CDMA
  UMTS (Universal Mobile Telecommunications System) from ETSI
UMTS
  UTRA (was: UMTS, now: Universal Terrestrial Radio Access)
  enhancements of GSM
    EDGE (Enhanced Data rates for GSM Evolution): GSM up to 384 kbit/s
    CAMEL (Customized Application for Mobile Enhanced Logic)
    VHE (virtual Home Environment)
  fits into GMM (Global Multimedia Mobility) initiative from ETSI
  requirements
    min. 144 kbit/s rural (goal: 384 kbit/s)
    min. 384 kbit/s suburban (goal: 512 kbit/s)
    up to 2 Mbit/s urban

## Slide 72: Frequencies for IMT-2000
IMT-2000
1850
1900
1950
2000
2050
2100
2150
2200
MHz
MSS

ITU allocation
(WRC 1992)
IMT-2000
MSS

Europe
China
Japan
North
America
UTRA
FDD 
UTRA
FDD 
T
D
D
T
D
D
MSS

MSS

DE
CT
GSM
1800
1850
1900
1950
2000
2050
2100
2150
2200
MHz
IMT-2000
MSS

IMT-2000
MSS

GSM
1800
cdma2000
W-CDMA
MSS

MSS

MSS

MSS

cdma2000
W-CDMA
PHS
PCS
rsv.

## Slide 73: IMT-2000 family
IMT-DS
(Direct Spread)
UTRA FDD
(W-CDMA)
3GPP
IMT-TC
(Time Code)
UTRA TDD
(TD-CDMA);
TD-SCDMA
3GPP
IMT-MC
(Multi Carrier)
cdma2000
3GPP2
IMT-SC
(Single Carrier)
UWC-136
(EDGE)
UWCC/3GPP
IMT-FT
(Freq. Time)
DECT
ETSI
GSM
(MAP)
ANSI-41
(IS-634)
IP-Network
IMT-2000
Core Network
ITU-T
IMT-2000
Radio Access
ITU-R
Interface for Internetworking
Flexible assignment of Core Network and Radio Access
Initial UMTS
(R99 w/ FDD)

## Slide 74: GSM, UMTS, and LTE Releases
Stages
  (0: feasibility study)
  1: service description from a service-user’s point of view
  2: logical analysis, breaking the problem down into functional elements and the information flows amongst them
  3: concrete implementation of the protocols between physical elements onto which the functional elements have been mapped
  (4: test specifications)
Note
  "Release 2000" was used only temporarily and was eventually replaced by "Release 4" and "Release 5"
Additional information:
  www.3gpp.org/releases
Rel | Spec version no. | Functional freeze date, indicative only
Rel-12 | 12.x.y | Stage 1 freeze March 2013
 |  | Stage 2 freeze December 2013
 |  | Stage 3 freeze June 2014, RAN: Sept. 2014
Rel-11 | 11.x.y | Stage 1 freeze September 2011
 |  | Stage 2 freeze March 2012
 |  | Stage 3 freeze September 2012
Rel-10 | 10.x.y | Stage 1 freeze March 2010
 |  | Stage 2 freeze September 2010
 |  | Stage 3 freeze March 2011
Rel-9 | 9.x.y | Stage 1 freeze December 2008
 |  | Stage 2 freeze June 2009
 |  | Stage 3 freeze December 2009
Rel-8 | 8.x.y | Stage 1 freeze March 2008
 |  | Stage 2 freeze June 2008
 |  | Stage 3 freeze December 2008
Rel-7 | 7.x.y | Stage 1 freeze September 2005
 |  | Stage 2 freeze September 2006
 |  | Stage 3 freeze December 2007
Rel-6 | 6.x.y | December 2004 - March 2005
Rel-5 | 5.x.y | March - June 2002
Rel-4 | 4.x.y | March 2001
R00 | 4.x.y | see note 1 below
 | 9.x.y | 
R99 | 3.x.y | March 2000
 | 8.x.y | 
R98 | 7.x.y | early 1999
R97 | 6.x.y | early 1998
R96 | 5.x.y | early 1997
Ph2 | 4.x.y | 1995
Ph1 | 3.x.y | 1992

## Slide 75: Licensing Example: UMTS in Germany, 18. August 2000
UTRA-FDD:
  Uplink 1920-1980 MHz
  Downlink 2110-2170 MHz
  duplex spacing 190 MHz
  12 channels, each 5 MHz
UTRA-TDD:
  1900-1920 MHz,
  2010-2025 MHz;
  5 MHz channels
Coverage of the population
  25% until 12/2003
  50% until 12/2005
Sum: 50.81 billion €

## Slide 76: UMTS architecture
Release 99 used here as starting point
  Shows the key differences
  Newer releases explained in the context of LTE
UTRAN (UTRA Network)
  Cell level mobility
  Radio Network Subsystem (RNS)
  Encapsulation of all radio specific tasks
UE (User Equipment)
CN (Core Network)
  Inter system handover
  Location management if there is no dedicated connection between UE and UTRAN
UTRAN
UE
CN
Iu
Uu

## Slide 77: UMTS domains and interfaces I
User Equipment Domain
  Assigned to a single user in order to access UMTS services
Infrastructure Domain
  Shared among all users
  Offers UMTS services to all accepted users
USIM
Domain
Mobile Equipment
Domain
Access
Network
Domain
Serving
Network
Domain
Transit
Network
Domain
Home
Network
Domain
Cu
Uu
Iu
User Equipment Domain
Zu
Yu
Core Network Domain
Infrastructure Domain

## Slide 78: UMTS domains and interfaces II
Universal Subscriber Identity Module (USIM)
  Functions for encryption and authentication of users
  Located on a SIM inserted into a mobile device
Mobile Equipment Domain
  Functions for radio transmission
  User interface for establishing/maintaining end-to-end connections
Access Network Domain
  Access network dependent functions
Core Network Domain
  Access network independent functions
  Serving Network Domain
    Network currently responsible for communication
  Home Network Domain
    Location and access network independent functions

## Slide 79: Questions & Tasks
  What defines the 3rd generation? What was the initial idea?
  What led to the different developments? – There are many reasons!
  Check www.3gpp.org/releases and understand the ideas of stages and releases!
  What was the focus of early UMTS on? How is this reflected in the spectrum?
  What is the problem of the condition “coverage of the population in %”?
  Why did most operators already using GSM pick UMTS as 3rd generation and cdmaOne operators cdma2000?

## Slide 80: Spreading and scrambling of user data
Constant chipping rate of 3.84 Mchip/s
Different user data rates supported via different spreading factors
  higher data rate: less chips per bit and vice versa
User separation via unique, quasi orthogonal scrambling codes
  users are not separated via orthogonal spreading codes
  much simpler management of codes: each station can use the same orthogonal spreading codes
  precise synchronization not necessary as the scrambling codes stay quasi-orthogonal
data1
data2
data3
scrambling
code1
spr.
code3
spr.
code2
spr.
code1
data4
data5
scrambling
code2
spr.
code4
spr.
code1
sender1
sender2

## Slide 81: OVSF (Orthogonal Variable Spreading Factor) coding
1
1,1
1,-1
1,1,1,1
1,1,-1,-1
X
X,X
X,-X
1,-1,1,-1
1,-1,-1,1
1,-1,-1,1,1,-1,-1,1
1,-1,-1,1,-1,1,1,-1
1,-1,1,-1,1,-1,1,-1
1,-1,1,-1,-1,1,-1,1
1,1,-1,-1,1,1,-1,-1
1,1,-1,-1,-1,-1,1,1
1,1,1,1,1,1,1,1
1,1,1,1,-1,-1,-1,-1
SF=1
SF=2
SF=4
SF=8
SF=n
SF=2n
...
...
...
...

## Slide 82: UMTS FDD frame structure
W-CDMA
1920-1980 MHz uplink
2110-2170 MHz downlink
chipping rate: 3.840 Mchip/s
soft handover
QPSK
complex power control (1500 power control cycles/s)
spreading: UL: 4-256; DL:4-512
0
1
2
12
13
14
...
Radio frame
Pilot
FBI
TPC
Time slot
666.7 µs
10 ms
Data
Data1
uplink DPDCH
uplink DPCCH
downlink DPCH
TPC
TFCI
Pilot
666.7 µs
666.7 µs
DPCCH
DPDCH
2560 chips, 10 bits
2560 chips, 10*2k bits (k = 0...6)
TFCI
2560 chips, 10*2k bits (k = 0...7)
Data2
DPDCH
DPCCH
FBI: Feedback Information
TPC: Transmit Power Control
TFCI: Transport Format Combination Indicator
DPCCH: Dedicated Physical Control Channel
DPDCH: Dedicated Physical Data Channel
DPCH: Dedicated Physical Channel
Slot structure NOT for user separation
but synchronization for periodic functions!

## Slide 83: Typical UTRA-FDD uplink data rates
User data rate [kbit/s] | 12.2 (voice) | 64 | 144 | 384
DPDCH [kbit/s] | 60 | 240 | 480 | 960
DPCCH [kbit/s] | 15 | 15 | 15 | 15
Spreading | 64 | 16 | 8 | 4

## Slide 84: UMTS TDD frame structure (burst type 2)
TD-CDMA
2560 chips per slot
spreading: 1-16
symmetric or asymmetric slot assignment to UL/DL (min. 1 per direction)
tight synchronization needed
simpler power control (100-800 power control cycles/s)
0
1
2
12
13
14
...
Radio frame
Data
1104 chips
Midample
256 chips
Data
1104 chips
Time slot
666.7 µs
10 ms
Traffic burst
GP
GP: guard period
96 chips
2560 chips

## Slide 85: UTRAN architecture
UTRAN comprises several RNSs
Node B can support FDD or TDD or both
RNC is responsible for handover decisions requiring signaling to the UE
Cell offers FDD or TDD
RNC: Radio Network Controller
RNS: Radio Network Subsystem
Node B
Node B
RNC
Iub
Node B
UE1
RNS
CN
Node B
Node B
RNC
Iub
Node B
RNS
Iur
Node B
UE2
UE3
Iu

## Slide 86: UTRAN functions
Admission control
Congestion control
System information broadcasting
Radio channel encryption
Handover
SRNS moving
Radio network configuration
Channel quality measurements
Macro diversity
Radio carrier control
Radio resource control
Data transmission over the radio interface
Outer loop power control (FDD and TDD)
Channel coding
Access control

## Slide 87: Core network: protocols
MSC
RNS
SGSN
GGSN
GMSC
HLR
VLR
RNS
Layer 1: PDH, SDH, SONET
Layer 2: ATM
Layer 3: IP
GPRS backbone (IP)
SS 7
GSM-CS
backbone
PSTN/
ISDN
PDN (X.25),
Internet (IP)
UTRAN
CN

## Slide 88: Core network: architecture
BTS
Node B
BSC
Abis
BTS
BSS
MSC
Node B
Node B
RNC
Iub
Node B
RNS
Node B
SGSN
GGSN
GMSC
HLR
VLR
  IuPS
  IuCS
Iu
CN
EIR
Gn
Gi
PSTN
AuC
GR

## Slide 89: Core network
The Core Network (CN) and thus the Interface Iu, too, are separated into two logical domains:
Circuit Switched Domain (CSD)
  Circuit switched service incl. signaling
  Resource reservation at connection setup
  GSM components (MSC, GMSC, VLR)
  IuCS
Packet Switched Domain (PSD)
  GPRS components (SGSN, GGSN)
  IuPS
Release 99 uses the GSM/GPRS network and adds a new radio access!
  Helps to save a lot of money …
  Much faster deployment
  Not as flexible as newer releases (5, 6, … 12, 13, 14, …)

## Slide 90: UMTS protocol stacks (user plane)
apps. &
protocols
MAC
radio
MAC
radio
RLC
SAR
Uu
IuCS
UE
UTRAN
3G
MSC
RLC
AAL2
ATM
AAL2
ATM
SAR
apps. &
protocols
MAC
radio
MAC
radio
PDCP
GTP
Uu
IuPS
UE
UTRAN
3G
SGSN
RLC
AAL5
ATM
AAL5
ATM
UDP/IP
PDCP
RLC
UDP/IP
UDP/IP
Gn
GTP
GTP
L2
L1
UDP/IP
L2
L1
GTP
3G
GGSN
IP, PPP,
…
IP, PPP,
…
IP tunnel
Circuit
switched
Packet
switched

## Slide 91: Questions & Tasks
  How do higher/lower data rates influence the robustness of the transmission in UMTS? How do typical applications fit to these effects?
  How does UTRA-FDD counteract the near-far effect?
  What is a drawback of OVSF? How is it compensated?
  How are different data streams from different users separated?
  Compare the UTRAN architecture with that of GSM. What is a major difference in the radio subsystem (BSS/RNS)? What is it used for?

## Slide 92: Support of mobility: macro diversity
Multicasting of data via several physical channels
Enables soft handover
FDD mode only
Uplink
simultaneous reception of UE data at several Node Bs
Reconstruction of data at Node B, SRNC or DRNC
Downlink
Simultaneous transmission of data via different cells
Different spreading codes in different cells
CN
Node B
RNC
Node B
UE

## Slide 93: Support of mobility: handover
From and to other systems (e.g., UMTS to GSM)
  This is a must as UMTS coverage is/was poor in the beginning
RNS controlling the connection is called SRNS (Serving RNS)
RNS offering additional resources (e.g., for soft handover) is called Drift RNS (DRNS)
End-to-end connections between UE and CN only via Iu at the SRNS
  Change of SRNS requires change of Iu
  Initiated by the SRNS
  Controlled by the RNC and CN
SRNC
UE
DRNC
Iur
CN
Iu
Node B
Iub
Node B
Iub

## Slide 94: Example handover types in UMTS/GSM
RNC1
UE1
RNC2
Iur
3G MSC1
Iu
Node B1
Iub
Node B2
Node B3
3G MSC2
BSC
BTS
2G MSC3
A
Abis
UE2
UE3
UE4

## Slide 95: Breathing Cells
GSM
  Mobile device gets exclusive signal from the base station
  Number of devices in a cell does not influence cell size
UMTS
  Cell size is closely correlated to the cell capacity
  Signal-to-nose ratio determines cell capacity
  Noise is generated by interference from
    other cells
    other users of the same cell
  Interference increases noise level
  Devices at the edge of a cell cannot further increase their output power (max. power limit) and thus drop out of the cell  no more communication possible
  Limitation of the max. number of users within a cell required
  Cell breathing complicates network planning

## Slide 96: Breathing Cells: Example

## Slide 97: UMTS services (originally)
Data transmission service profiles
Virtual Home Environment (VHE)
  Enables access to personalized data independent of location, access network, and device
  Network operators may offer new services without changing the network
  Service providers may offer services based on components which allow the automatic adaptation to new networks and devices
  Integration of existing IN services
Circuit switched
16 kbit/s
Voice
SMS successor, E-Mail
Packet switched
14.4 kbit/s
Simple Messaging
Circuit switched
14.4 kbit/s
Switched Data
asymmetrical, MM, downloads
Circuit switched
384 kbit/s
Medium MM
Low coverage, max. 6 km/h
Packet switched
2 Mbit/s
High MM
Bidirectional, video telephone
Circuit switched
128 kbit/s
High Interactive MM
Transport mode
Bandwidth
Service Profile

## Slide 98: Early 3G Networks: Japan
FOMA (Freedom Of Mobile multimedia
Access) in Japan
Examples for FOMA phones

## Slide 99: Early 3G networks: Australia
cdma2000 1xEV-DO in Melbourne/Australia
Examples for 1xEV-DO devices

## Slide 100: Isle of Man – Start of UMTS in Europe as Test

## Slide 101: UMTS in Monaco

## Slide 102: Early UMTS in Europe
Vodafone/Germany
Orange/UK

## Slide 103: Some current GSM enhancements
EMS/MMS
  EMS: 760 characters possible by chaining SMS, animated icons, ring tones, was soon replaced by MMS (or simply skipped)
  MMS: transmission of images, video clips, audio
    see WAP 2.0 – not really successful, typically substituted by email with attached multimedia content
  Today, more and more IP-based messaging used, less specialized services offered by the network
EDGE (Enhanced Data Rates for Global [was: GSM] Evolution)
  8-PSK instead of GMSK, up to 384 kbit/s
  new modulation and coding schemes for GPRS  EGPRS
    MCS-1 to MCS-4 uses GMSK at rates 8.8/11.2/14.8/17.6 kbit/s
    MCS-5 to MCS-9 uses 8-PSK at rates 22.4/29.6/44.8/54.4/59.2 kbit/s

## Slide 104: Some current UMTS enhancements
HSDPA (High-Speed Downlink Packet Access)
  initially up to 10 Mbit/s for the downlink, later > 20 Mbit/s using MIMO- (Multiple Input Multiple Output-) antennas
  can use 16-QAM instead of QPSK (ideally > 13 Mbit/s)
  user rates e.g. 3.6 or 7.2 Mbit/s
HSUPA (High-Speed Uplink Packet Access)
  initially up to 5 Mbit/s for the uplink
  user rates e.g. 1.45 Mbit/s
HSPA+ (Evolved HSPA)
  Rel-7/Rel-8/Rel-9/…
  Downlink 28/42/84/> 100 Mbit/s
  Uplink 11/23/>23 Mbit/s
  2x2 MIMO, 64 QAM
Dual-/Multi-Carrier HSPA (DC-/MC-HSPA)
  Connect 2 (Rel-8/9) or more carriers (Rel-11) e.g. of two cells offering up to 672 Mbit/s (4x4 MIMO)

## Slide 105: Questions & Tasks
  Compare the handovers in GSM with the ones in UMTS. Why are they called hard or soft, respectively?
  How much is the core network aware of the type of handover?
  What are the consequences of introducing IP-based packet transmission?
  What is the key to higher data rates in UMTS?
  While the data rates increased over time, the delay remained more or less constant at about 100-150 ms from a mobile device to the base station. What problem arises if e.g. downloading content using TCP via these fast connections? Think of congestion avoidance/RTT!

## Slide 106: Long Term Evolution (LTE)
Initiated in 2004 by NTT DoCoMo, focus on enhancing the Universal Terrestrial Radio Access (UTRA) and optimizing 3GPP’s radio access architecture
Targets: Downlink 100 Mbit/s, uplink 50 Mbit/s, RTT<10ms
2007: E UTRA progressed from the feasibility study stage to the first issue of approved Technical Specifications
2008: stable for commercial implementation
2009: first public LTE service available (Stockholm and Oslo)
2010: LTE starts in Germany
LTE is not 4G – sometimes called 3.9G
  Does not fulfill all requirements for IMT advanced

## Slide 107: LTE High-level Architecture
User Equipment (UE)
  Mobile Termination (MT) handles wireless/mobile communication
  Terminal Equipment (TE) handles data streams
  Universal Integrated Circuit Card (UICC): the SIM for LTE, runs the USIM
Evolved UMTS Terrestrial Radio Access Network (E-UTRAN)
  comprises the eNodeBs (i.e. the base stations including controllers)
  interfaces to the EPC via a user interface (S1-U) and signaling interface (S1-MME)
Evolved Packet Core (EPC)
  comprises the central database for subscribers, equipment identity
  routes data to/from other Packet Data Networks (PDN)
  functions for policing, charging, authentication
UE
E-UTRAN
EPC
PDNs
Uu
S1-MME
S1-U
SGi

## Slide 108: Initial typical data rates (Release 8)
UE Category | Max. data rate downlink | Max downlink MIMO | Max data rate uplink
1 | 10.3 | 1 | 5.2
2 | 51.0 | 2 | 25.5
3 | 102.0 | 2 | 51.0
4 | 150.8 | 2 | 51.0
5 | 299.6 | 4 | 75.4
Higher (and lower) data rates with LTE advanced!

## Slide 109: QoS Classes
3GPP TS 23.203
(only part shown here)

## Slide 110: May 2011, Berlin gets LTE

## Slide 111: Fast growth rates of LTE

## Slide 112: LTE will stay for a while
source: Heise-Verlag, c’t 15/2019

## Slide 113: LTE today – THE global standard (only 9 countries without LTE in 2019)
May 2020
797 operators
325 LTE advanced/pro
210 VoLTE networks
106 NB-IoT networks
80 operators offering 5G
https://gsacom.com/technology/5g/
“LTE-Not-Spots” (source: GSA/Heise-Verlag, c’t 15/2019)

## Slide 114: Key LTE features
Simplified network architecture compared to GSM/UMTS
  Flat IP-based network replacing the GPRS core, optimized for the IP-Multimedia Subsystem (IMS), no more circuit switching
Network should be in parts self-organizing
Scheme for soft frequency reuse between cells
  Inner part uses all subbands with less power
  Outer part uses pre-served subbands with higher power
Much higher data throughput supported by multiple antennas
Much higher flexibility in terms of spectrum, bandwidth, data rates
Much lower RTT – good for interactive traffic and gaming
Smooth transition from W-CDMA/HSPA, TD-SCDMA and cdma2000 1x EV-DO – but completely different radio!
Large step towards 4G – IMT advanced
See www.3gpp.org for all specs, tables, figures etc.!

## Slide 115: High flexibility
E-UTRA (Evolved UMTS Terrestrial Radio Access)
  Operating bands 700-2700MHz
  Channel bandwidth 1.4, 3, 5, 10, 15, or 20 MHz
  TDD and FDD
Modulation
  QPSK, 16QAM, 64QAM
Multiple Access
  OFDMA (DL), SC-FDMA (UL)
Peak data rates (cat 5 UE)
  300 Mbit/s DL (4x4 MIMO, 20 MHz)
  75 Mbit/s UL
  Depends on UE category
Cell radius
  From <1km to 100km
Mobility
  up to 350km/h
source: 3GPP TS 36.101

## Slide 116: Questions & Tasks
  Why is LTE such a world-wide success? Think of parameters, architecture …
  Name high-level differences between LTE and GSM/GPRS/UMTS! What do they have in common?
  What is the idea of soft frequency reuse?

## Slide 117: LTE architecture
S-GW
UE2
eNode B
eNode B
eNode B
eNode B
eNode B
UE1
E-UTRAN
EPC (Evolved Packet Core)
X2-U/-C
X2-U/-C
X2-U/-C
X2-U/-C
S1-U
S1-U
MME
S1-MME
S1-MME
Mobility Management Entity Serving Gateway
Packet-data network Gateway Home Subscriber Server
Policy and Charging Rules Function
S11
MME
S10
P-GW
S5 S8 (roaming)
Internet,
Operators…
Uu
Uu
PCRF
HSS
SGi
S6
S7
Rx+
GPRS
S3
S4

## Slide 118: Components of the LTE architecture I – Evolved-UTRAN
eNode B
Radio resource management
QoS management
Interference management
Admission control
Signal measurements
Scheduling/resource allocation
IP header compression
Encryption
Comprises former NodeB plus RNC functionality, now for LTE to reduce latency
UE communicates only with one eNodeB, the serving eNodeB
Connection to EPC (via S1-U and S1-MME) and to other eNodeBs (via X2-U and X2-C)
Home eNodeBs possible (e.g. to create a femtocell at home)
UE2
eNode B
eNode B
eNode B
eNode B
eNode B
UE1
E-UTRAN
X2-U/-C
X2-U/-C
X2-U/-C
X2-U/-C
Uu
Uu

## Slide 119: Components of the LTE architecture II - EPC (Evolved Packet Core)
MME (Mobility Management Entity)
Signaling between UE and EPC
Security, Mobility Handling
Bearer Control
S-GW (Serving Gateway)
Mobility Anchor for all user IP packets
Buffering during UE paging
Charging, lawful interception
P-GW (PDN Gateway)
IP address allocation for the UE
Packet filtering, QoS enforcement
HSS (Home Subscriber Server)
Subscriber information (allowed PDNs, QoS profile, roaming restrictions)
MME identity of current location
Includes authentication center
PCRF (Policy and Charging Rules Function)
QoS authorization, policy control, controls flow-based charging
S-GW
EPC (Evolved Packet Core)
S1-U
S1-U
MME
S1-MME
S1-MME
S11
MME
S10
P-GW
S5 S8 (roaming)
Internet,
Operators…
PCRF
HSS
SGi
S6
S7
Rx+
GPRS
S3
S4

## Slide 120: LTE protocol stack (user plane)
apps. &
protocols
MAC
radio
MAC
radio
PDCP
GTP-U
LTE Uu
S1-U
UE
eNodeB
S-GW
RLC
L2
L1
L2
L1
UDP/IP
PDCP
RLC
UDP/IP
UDP/IP
S5/S8
GTP-U
GTP-U
L2
L1
UDP/IP
L2
L1
GTP-U
P-GW
IP
IP
IP tunnel
Packet
switched
only!

## Slide 121: LTE frame structure
0
1
2
7
8
9
...
Radio frame (10 ms)
Subframe (1 ms)
FDD
UL
DL
0
1
2
7
8
9
...
TDD
...
Synchronization is part of subframe 0 and 5
UL/DL
Downlink Pilot Time Slot (data plus pilot signal)
0
1
2
7
8
9
...
Guard Period
Uplink Pilot Time Slot (random access plus pilot signal)

## Slide 122: LTE multiple access
Scheduling of UEs in time and frequency (very simplified) using resource blocks (180kHz in 1 ms)
t
f
UE1
UE2
UE3
UE4
UE1
UE1
UE2
UE4
UE3
UE4
UE1
UE1
UE2
UE2
UE2
UE1
UE1
UE4
UE2
UE1
UE1
UE3
UE3
UE2
UE1
UE1
UE3
UE3
UE4
UE4
180 kHz
1 ms

## Slide 123: TDM requires Timing Alignment
Similar to GSM – the further away a UE from the eNodeB is, the earlier it transmits
Configurable at a granularity of 0.52µs from 0 to 0.67 ms (corresponding to a max. cell radius of 100 km)
UE1
UE2



t1
t2



t1
t2


## Slide 124: LTE handover via S1
Source: The LTE Network Architecture, Strategic White Paper, Alcatel Lucent 2009
S-GW
eNode B
eNode B
X2-U/-C
S1-U
MME
S1-MME
MME
Uu
S-GW
S1-U
UE
S1-MME

## Slide 125: LTE handover via X2 interface
Source: The LTE Network Architecture, Strategic White Paper, Alcatel Lucent 2009
S-GW
eNode B
eNode B
X2-U/-C
S1-U
MME
S1-MME
MME
Uu
S-GW
S1-U
UE
S1-MME
Seamless or lossless handovers possible as well as multiple target eNodeBs

## Slide 126: Questions & Tasks
  Compare the architecture of LTE/UMTS/GSM – what is new, what is basically the same?
  What is the purpose of the X2 connections between eNodeBs? How can LTE support seamless / lossless handover?
  How can LTE guarantee data rates, delays?
  Compare the multiplexing/multiple access in LTE with UMTS/GSM – differences/similarities?

## Slide 127: IMT Advanced – from www.itu.int
Key features of ´IMT-Advanced´:
a high degree of commonality of functionality worldwide while retaining the flexibility to support a wide range of services and applications in a cost efficient manner;
compatibility of services within IMT and with fixed networks;
capability of interworking with other radio access systems;
high quality mobile services;
user equipment suitable for worldwide use;
user-friendly applications, services and equipment;
worldwide roaming capability; and,
enhanced peak data rates to support advanced services and applications (100 Mbit/s for high and 1 Gbit/s for low mobility were established as targets for research).
These features enable IMT-Advanced to address evolving user needs and the capabilities of IMT-Advanced systems are being continuously enhanced in line with user trends and technology developments.

## Slide 128: LTE Advanced (Pro)
GSM – UMTS - LTE
  LTE advanced as candidate for IMT-advanced, 3GPP Rel 10/11/12
  LTE-A Pro: 4.5G/Pre 5G…, 3GPP Rel 13/14 – steps towards 5G
Worldwide functionality & roaming, compatibility of services
Interworking with other radio access systems (e.g. WiFi), use of unlicensed spectrum
Enhanced peak data rates to support advanced services and applications (100 Mbit/s for high and 1/3 Gbit/s for low mobility)
3GPP will be contributing to the ITU-R towards the development of IMT-Advanced via its proposal for LTE-Advanced.
Relay Nodes to increase coverage, Machine-Type-Communications, Public Safety Features (e.g. D2D)
100 MHz bandwidth (5x LTE with 20 MHz), carrier aggregation, increased battery life …

## Slide 129: LTE for the Internet of Things I
LTE as scaleable platform
Source: www.qualcomm.com

## Slide 130: LTE for the Internet of Things II
Low power LTE – run-times > 10 years based on battery
Source: www.qualcomm.com

## Slide 131: Questions & Tasks
  What is “evolutionary” in LTE?
  How does LTE reflect the variety of different demands?
  Check out the current status of LTE and the smooth transition towards 5G e.g. on 3GPP!